## Slide 1: Literature Review VI-SLAM VINS-Mono
Ritvik Pandey
  Intern H402743

## Slide 2: This presentation will cover
VIO Techniques
  Standard modules
  Working of these modules
  Filtering based VIO
VINS-Mono
  Addressing problems
  Overview of steps
  Working and formulations
Temporal caliberation
  Why and how?.
  Explaining VINS in application
To present the general picture of SLAM algorithms and their working in detail
Overview of SLAM
  Principle, Need
  Setup, VIO

## Slide 3: Overview: SLAM
Mapping
(What does the world look like?)
  Requires access to observe and recognize landmarks
    Camera, Lidar
Localization
(Where am I?)
  Requires good odometry data. (where and how much I moved?)
    IMU
The two essential components of SLAM

## Slide 4: Overview: Key modules
Sensors and Pre-processing
  Data from camera, LIDAR, IMU are fetched
  Data is correspondingly pre-processed to be fed to successive modules
Feature detection and matching
  Relation between current and previous frame
  Keeps track of intermediate motion
Pose estimation and Global mapping
  These intermediate motions are then used to locate drone in global frame
Loop closure and Bundle adjustment
  Detecting previously visited area
  Local and global data is adjusted again based on reconfigured values in bundle form
Any SLAM comprises of these modules
OPTIONAL

## Slide 5: Overview: VI-SLAM
Visual data
Monocular/Stereo camera
  Has very less chances of error as drone is physically present there
  Lacks Scale measurement
  Low frequency
Inertial data
IMU measurements
  Fast data
  Has scale (metric)
  Significant error in form of bias associated
Challenges
  How to integrate visual and inertial data
  How to compensate time delay in receiving the data
  How to deal with old data and large deviation
  Minimize computation to make it real time
  What if we loose track
  How to detect and correct our estimates when visit a place again

## Slide 6: VIO Techniques: Classification
Filtering based:
IMU to assist visual-only SLAM
Comprises of all the techniques which use some kind of filtering algorithm like
EKF (extended Kalman filter for non-linear problems)
Ellipsoidal Kalman filter
Dynamic Linear model
Faster and computationally cheap
Has larger error and memory consumption
Fail to recover from lost state
Optimization based:
Error from both IMU and visual data is jointly minimized
We calculate error from tracking of features of visual data and IMU data error to match with it, we then modify the estimates to minimize this joint error
Computationally intensive
Less error and memory requirement
May or may not recover lost state

## Slide 7: Filtering Based techniques: Overview
Feature Extraction and Tracking
  Keypoints and Descriptor
  Uses camera feed
  - SIFT, SURF : Binacular-Vision SLAM
- Harris Detector: Mono-SLAM
- ORB: ORB-SLAM
Dynamic Observational Model
  Control and State estimation using filtering pipeline
  Uses IMU data
    Extended Kalman Filter for non-linear problems
Two components of filtering based techniques

## Slide 8: Feature Extraction and Tracking
Feature Extraction
  Keypoints (corner, change in first/second order derivative at a point, local maxima/minima)
  The value at which keypoint selected is its descriptor
  Feature Tracking
  Descriptors are matched with keypoints from other images and warping matrix is calculated.
VINS uses BRIEF descriptor and KLT sparse optical tracker
SIFT, SURF : Binacular-Vision SLAM
Harris Detector: Mono-SLAM
ORB: ORB-SLAM

## Slide 9: Filtering: Dynamic observational model
Usage
  Serves as both control and state estimation of the filtering pipeline
  Need
  In real world, data arrives with lag so an estimation is need of state of drone at each moment in time
Updating the new estimate and variance
=
IMU measurement at any time T
= f(, ) +

## Slide 10: Filtering: Dynamic observational model
Usage
  Serves as both control and state estimation of the filtering pipeline
  Need
  In real world, data arrives with lag so an estimation is need of state of drone at each moment in time
Prediction of state using previous state and control vector with noise
=
IMU measurement at any time T
= f(, ) +
Prediction Phase

## Slide 11: Filtering: Dynamic observational model
Usage
  Serves as both control and state estimation of the filtering pipeline
  Need
  In real world, data arrives with lag so an estimation is need of state of drone at each moment in time
Prediction of state using previous state and control vector with noise
=
IMU measurement at any time T
= f(, ) +

## Slide 12: VINS-MONO Modules and working

## Slide 13: VINS-Mono: Introduction
Local odometry
What is happening locally
Optimizing for local odometry errors
Relation with previous few frames and using intermediate IMU data
Global odometry
What is global picture
Taking previously accumulated errors in account
Relation with frames acquired long time back and visiting same point
As new frames arrive, we push older keyframes to pose graph
State of the art tightly coupled non-linear optimization based SLAM
GLOBAL POSE GRAPH
SLIDING WINDOW

## Slide 14: VINS-Mono: Introduction
Pre-processing
  Camera and IMU data is pre-processed and corrected for error before it is sent to any other module
Initialization
  Getting initial estimation of position, velocity, orientation and scale
Core VIO algorithms
  Successively updating state from previous state and new visual and Imu feeds.
Relocalization
  On loop closure, the sliding window is optimized for newer position in space based on closure constraints
Global pose graph optimization
  After relocalization, previous pose graph must be adjusted accordingly
Temporal Caliberation
  Additionally, time delay b/w visual and IMU data must be estimated
State of the art tightly coupled non-linear optimization based SLAM

## Slide 15: VINS-Mono: Introduction
State of the art tightly coupled non-linear optimization based SLAM
Pre-Processing
Camera
IMU data
Initialization
or
Core-VIO
No initial estimate
Initialization
+ failure detection
Starting estimate
for Core-VIO
Previous estimates
Core-VIO algorithm
New estimates
Relocalization + Pose graph Optimization
Previously visited place
(Loop detected)
Adjusted local and global odometry data
First Data
Adjustment for drift accumulated
New Data

## Slide 16: VINS-Mono: Pre-Processing
State of the art tightly coupled non-linear optimization based SLAM
Camera
IMU data
Feature detection and Tracking
IMU Pre-integration
Key-point selection
Key-point Tracking
IMU bias estimation
and parameterization
VISION PRE-PROCESSING
Feature Detection: BRIEF descriptor (rotational in-variant)
Feature Tracking: KLT sparse optical flow
Keypoint Outlier rejection: RANSAC + uniform special distance between keypoints
Keyframe selection: average parallax from previous keyframe more than threshold. Any image not a keyframe is thrown and only IMU data kept.

## Slide 17: VINS-Mono: Pre-Processing
IMU Pre-Integration
IMU PRE-INTEGRATION
Why is it required
What happens in this process
Mathematical Formulation
Accelerometer and Gyroscopic measurements from IMU
Translation vector, Velocity vector and Rotation vector from body frame to world frame

## Slide 18: VINS-Mono: Pre-Processing
IMU Pre-Integration
Accelerometer and Gyroscopic measurements from IMU
Translation vector, Velocity vector and Rotation vector from body frame to world frame
Why pre-integration?
NOTE: All these vectors use reference from previous measurement so if we find that an old estimation was slightly wrong, we need to re-propogate back to all those steps if same formulae are used.

## Slide 19: VINS-Mono: Pre-Processing
IMU Pre-Integration
New vector estimates which do not directly use previous measurements
Changing from world to body frame:
Here, α (alpha), β (beta), γ (gamma) only depend on bias and not on any previous state
So we need not to re-propogate whenever our bias estimate “b” changes

## Slide 20: VINS-Mono: INITIALIZATION initial estimate of position, orientation, velocity, scale, bias
Finally, position, velocity are scaled and provided to core-VIO algorithm for successive update
Structure from Motion (SfM)
Visual-only SLAM
  Gives upto scale estimates using 5-point algorithm in first camera frame ()
  It gives line (in 3D space) on which a feature would lie. Only thing it requires now is scale.
Visual-Inertial Alignment
Using visual data for bias correction
  Optimizes rotational error between 2 consecutive frames to give gyroscopic bias estimation (gives gamma)
  Alpha, beta are written in terms of scale
Final optimizing step for scale
Optimizing for scale to minimize error in measurement
  We have gamma and alpha, beta are written in terms of scale. Now the error between current and previous state (in terms of scale) is minimized to give us scale measurement

## Slide 21: VINS-Mono: INITIALIZATION initial estimate of position, orientation, velocity, scale, bias
From SfM
Equation governing translation and rotation in camera frame
Alpha/Beta in terms of scale and IMU readings
Error optimization cost for bias estimation
From IMU pre-integration
Now we have good estimate of gamma and alpha, beta are written in terms of scale. The reading (z) at any given frame can be written as
OPTIMIZATION 1
OPTIMIZATION 2
Gives gamma
Gives Scale

## Slide 22: VINS-Mono: Core VIO Algorithm
Using previous state and new visual and IMU data to update the state estimate
Sliding Window
Priori
This module works only on Sliding Window part
If second latest image not a keyframe: its image data is thrown and only IMU kept. No frame marginalized
If second latest image is a keyframe: oldest frame in sliding window marginalized (converted to priori)
AIM: Keep latest and spatially separated keyframes in the window
Failure Detection and Bundle Adjustment
marginalized

## Slide 23: VINS-Mono: Core VIO Algorithm
Using previous state and new visual and IMU data to update the state estimate
State vector in sliding window can be represented as:
: inverse distance to feature
: IMU reading at frame in window
: camera to body vector
Priori
This module works only on Sliding Window part
Sliding Window

## Slide 24: VINS-Mono: Core VIO Algorithm
Using previous state and new visual and IMU data to update the state estimate
State vector in sliding window can be represented as:
: inverse distance to feature
: IMU reading at frame in window
: camera to body vector
Optimization function to be satisfied at each timestep
Error due to prior information
IMU residual error
Visual measurement residual error

## Slide 25: VINS-Mono: Core VIO Algorithm
Using previous state and new visual and IMU data to update the state estimate
IMU residual error
Change in IMU states and bias estimates from previous frame to this frame by pre-integration step
Visual Measurement residual error
What does it all mean?
It is just the scaled camera reprojection error of a feature
Error = Scale*(expected reprojection – true)
P : unit vector along reprojection
Observed
Expected

## Slide 26: VINS-Mono: Relocalization v/s Pose Graph
Occurs at loop closure
Every effort is made to minimize error but still some drift occurs. When we visit a location again, our past knowledge and current position can help us correct for those drifts. Correcting those drifts in sliding window is Relocalization and thereby adjusting previous data according to it is Global pose graph optimization

## Slide 27: VINS-Mono: Relocalization
Relocalization has 2 steps:
Loop detection: DBoW2 (Database Bag of Words representation of image features indexed for fast retrieval)
Optimization
feature observed previously in frame
Hence apart from usual cost function for sliding window, we now have a term which constraints us with loop connections to give us new estimated state and thus minimizing the overall drift.

## Slide 28: VINS-Mono: Global Pose Graph Optimizatio
As we have already relocalized the sliding window, the pose graph looks like image 5
4-Dof pose graph optimization:
Done according to sequential and loop closure edges residual error
Sequential edges
Loop edges
Pose Graph

## Slide 29: VINS-Mono: Working
Every /Scene data goes to /feature_tracker (pre-processing) and /pose_graph (detect loop closure)
If any matched points from previous poses, /pose_graph gives it to /vins_estimator (VIO-core) to optimize for it
All marginalized keyframes are saved in /pose_graph
Currently, we have set VINS to receive IMU data from mavros (can be made to take from airsim too)
Feature tracker tells /vins_estimator to restart if it looses track by a separate channel /feature_tracker/restart

## Slide 30: VINS-Mono: Temporal Caliberation
IMU and camera measurement don’t arrive at the same time, hence an estimate of time delay () is required
Expected location of feature considering time delay
New state function
Using same optimization cost function as before but with a newer state function